## Slide 1: Bore capability review: not ready for PPAP yet, but fixable
CNC brake caliper bore Ø 42.000 ± 0.025 mm · 3 machines · Jan–Jun 2026
For the Quality Manager · prepared by Areej Alsobh · synthetic practice dataset
Notes: Purpose: answer whether the bore process can meet the customer's Cpk/Ppk >= 1.33 requirement for the PPAP review, why not, and what to fix first. Data: 22,500 bore measurements, production and defect logs, tool changes and material lots from January to June 2026.

## Slide 2: The answer: not capable yet, but the machines can do it
0 of 3
machines meet Ppk ≥ 1.33 over Jan–Jun
Ppk 1.10 · 0.93 · 0.96
CNC-01 · CNC-02 · CNC-03
The machines are capable short-term
Cp 1.44–1.63 and well centred: the parts made together are consistent.
Capability is lost over time
Tool wear drifts the bore 0.014 mm per tool life; 28–36% of capability is lost (Cpk → Ppk).
A fix is already proven
With tool-wear compensation, CNC-01 reached Ppk 1.55 in June.
Decision needed: approve the roll-out of tool-wear compensation to CNC-02 and CNC-03.
Notes: Bottom line first. Over the full period no machine meets the customer's 1.33. But the gap between Cpk (short-term) and Ppk (long-term) shows the machines themselves are capable; the loss comes from drift over time. One machine already shows the fix works.

## Slide 3: Every machine loses capability over time: Cpk passes, Ppk fails
Chart: 
| CNC-01 | CNC-02 | CNC-03
Cpk (short-term) | 1.57 | 1.47 | 1.33
Ppk (long-term) | 1.1 | 0.93 | 0.96
Target 1.33 | 1.33 | 1.33 | 1.33
What the gap means
Cpk uses the spread of 5 parts made together: what the machine can do.
Ppk uses all parts over six months: what the customer received.
The process is not in statistical control, so Ppk is the honest figure for the customer.
Notes: Cpk 1.57 / 1.47 / 1.33 vs Ppk 1.10 / 0.93 / 0.96. Means are 41.998-41.999, so centring is not the problem (Cpk only 3-8% below Cp). The 28-36% loss from Cpk to Ppk is drift over time. CNC-03 Cpk is 1.3268: just below, not 1.33.

## Slide 4: Root cause 1: tool wear shrinks the bore 0.014 mm per tool life
Chart: Hours since tool change
| 0–6 | 6–12 | 12–18 | 18–24 | 24–30 | 30–36 | 36–42 | 42–48 | 48–54 | 54–60 | 60–66 | 66–72
Average bore diameter | 42.0057 | 42.0046 | 42.0032 | 42.002 | 42.0012 | 42.0001 | 41.9989 | 41.9977 | 41.9962 | 41.9952 | 41.994 | 41.9929
Nominal 42.000 | 42 | 42 | 42 | 42 | 42 | 42 | 42 | 42 | 42 | 42 | 42 | 42
0.014 mm
drift over a 72 h tool life: 28% of the tolerance
27–28%
of subgroups outside the X̄ control limits (0.3% expected)
32 h
until a new tool's average falls below nominal
Notes: Average bore by tool age on normal data (abnormal periods excluded). A new tool starts at about 42.006 mm and the bore shrinks 0.000193 mm per hour. This sawtooth is visible on every machine's X-bar chart: a jump up at every scheduled tool change, then a slow drift down. It is the main reason 65-73% of subgroups trigger a Western Electric rule.

## Slide 5: Root cause 2: a wrong offset ran CNC-02 high for 10 days
Chart: Subgroup mean (mm)
CNC-02 X̄ chart, 9 Mar – 3 Apr · red dashed = control limits
New tools on 16, 19 and 24 March started 0.013 mm high.
The wear rate was normal: the setup was wrong, not the tool.
The offset correction on 25 March fixed it mid-tool.
11 parts above the USL, all on those days.
Notes: Evidence: in the X-bar chart with tool changes, each scheduled change on 16, 19 and 24 March started a new tool around 42.018-42.021 instead of about 42.005, with the usual wear slope. The 'Offset correction' logged on 25 March at 10:00 dropped the level straight back. SQL: oversize defects only on those days. Action: first-part check after every tool change.

## Slide 6: Two more events: a slow reaction and a wider night-shift spread
CNC-01 tool breakage · 12 May, shift B
2.5 h
from the first SPC signal to the tool change
15:00: X̄ fell to 41.976 mm (LSL 41.975); X̄ and R both signalled
17:30: tool replaced, process back to normal at once
34 undersize + 30 surface-finish defects that day
Action: stop and inspect at the first out-of-control signal
CNC-03 night shift · from 1 April
1.6×
wider part-to-part spread (Levene's test, p < 0.001)
Started when a new operator (6 months' experience) replaced one with 7 years
Shifts A and B unchanged
20 of CNC-03's 24 out-of-spec parts
Action: onboarding and standard work, not blame
Notes: Breakage: both charts flagged the 15:00 subgroup, but the tool was replaced only at 17:30. A rule to react to the first signal would have saved one subgroup of production. Night shift: compared within-subgroup deviations (tool wear removed) between OP-07 and OP-11; standard deviation 0.0046 vs 0.0075 mm. The data shows when it changed, not why: treat it as an onboarding gap, not individual fault.

## Slide 7: Root cause 3: one over-hard material lot caused the May spike
Chart: Defect rate by month (per 1,000 parts)
| Jan | Feb | Mar | Apr | May | Jun
Defects per 1,000 parts | 9.14 | 8.37 | 10.72 | 11.3 | 56.08 | 10.15
195
defects per 1,000 parts on lot L-2026-041 (other lots 7–16)
242 HB
hardness of lot 041; every other lot 199–213 HB
137 of 140
rough parts (Ra > 1.6 µm) came from this one lot
Without lot 041, roughness PPU = 1.37 (passes). The same supplier (Kovar) also has chronic porosity: 3.87 per 1,000 vs 1.50 and 1.34.
Notes: Lot L-2026-041 from SUP-02 Kovar Castings was used 25-29 May. Its hardness (242 HB) is far outside the normal range. Across normal lots the hardness-roughness relationship is weak (r = 0.49 without lot 041, r = 0.95 with it), so the issue is this one outlier lot. Actions: hardness check at incoming inspection with a reject limit, supplier corrective action request to Kovar, containment check for shipped parts.

## Slide 8: Prioritise by cost: porosity is 4th by count but 1st by cost
Chart: Share of defective parts (count)
| Surface finish | Burr | Chatter marks | Porosity | Undersize bore | Oversize bore
Share of defective parts (count) | 36.9 | 23.4 | 16 | 11.9 | 8.6 | 3.3
Chart: Share of defect cost (€)
| Porosity | Surface finish | Burr | Chatter marks | Oversize bore | Undersize bore
Share of defect cost (€) | 34.4 | 24.3 | 15.4 | 10.6 | 9.6 | 5.7
€28,578 total defect cost (scrap €12,580 · rework €15,998). Porosity parts are scrapped at €18.50; most other defects are reworked at €4.20.
Notes: Defect Pareto from SQL and Power BI. 4,489 defective parts out of 253,374 produced (17.7 per 1,000). Ranking by count would point at surface finish (mostly the one bad lot week); ranking by cost points at porosity, which is linked to the Kovar supplier.

## Slide 9: The fix works: wear compensation lifted CNC-01 to Ppk 1.55
Chart: Ppk before and after 1 June
| CNC-01 | CNC-02 | CNC-03
Jan–May | 1.05 | 0.94 | 0.97
June | 1.55 | 0.93 | 0.9
Target 1.33 | 1.33 | 1.33 | 1.33
Why we trust it
Overall spread −31% (Levene's test, p < 0.001).
Control group: CNC-02 and CNC-03 did not improve, so it was not a good month.
Part-to-part spread (R) unchanged: only the drift disappeared, the fingerprint of wear compensation.
Not yet documented; one month of data.
Notes: From 1 June the sawtooth almost disappears on CNC-01: drift within a tool life fell from about 0.013-0.017 mm to 0.003-0.009 mm. The change is not in the tool change log, so the first step is to document what was set up. One month is enough to see the effect but not to prove it lasts: keep monitoring and recalculate the control limits.

## Slide 10: Recommended actions, in priority order
# | Action | Addresses | Expected impact
1 | Roll out tool-wear compensation to CNC-02, then CNC-03; verify each with before/after Ppk | Tool wear (all machines) | Ppk towards 1.4–1.55, as on CNC-01
2 | First-part check after every tool change | Offset errors (CNC-02, March) | No more 10-day shifts after a setup error
2 | Incoming hardness check with a reject limit; corrective action request to Kovar | Lot 041, chronic porosity | Roughness PPU 1.37; lower scrap cost
2 | Skill matrix, work instruction and pairing before solo night shifts | CNC-03 night-shift spread | R back to ≈ 0.012 mm
3 | Stop and inspect at the first SPC signal | Late reaction (CNC-01 breakage) | Contain problems hours earlier
3 | Document the CNC-01 change; recalculate its control limits | Change management | Charts that detect new problems
Fallback if compensation is not possible: change tools every 48 h and set the new-tool offset ≈ 0.002 mm lower (Pp ≈ 1.41–1.44).
Notes: Priority 1 removes the biggest single cause on every machine. A shorter tool-change interval alone does not raise Ppk because the average moves towards the USL; it only works with re-centring, and costs more tools and more tool-change risk.

## Slide 11: Path to the PPAP review
Decision today: approve the wear-compensation roll-out and the first-part check.
Weeks 1–2
Document the CNC-01 set-up; pilot on CNC-02; start first-part checks
Weeks 3–4
Roll out to CNC-03; night-shift onboarding; hardness check at goods-in
Weeks 5–8
New capability study on all machines; new control limits; PPAP submission
Notes: Target: re-run the capability study with at least 4 weeks of data after the changes, with new control limits, before submitting PPAP.

## Slide 12: Appendix: data and method
Data
22,538 measurements (5 parts every 2 h per machine), production log, defect log, tool changes, material lots. Synthetic dataset built for practice.
SQL (MySQL)
Profiling and cleaning; overall quality; defect Pareto; rates by machine, shift and month; lot and supplier scorecard; tool-change windows.
Python
X̄-R charts and Western Electric rules; Cp, Cpk, Pp, Ppk; Levene's test; correlation; before/after study; tool-wear regression.
Power BI
Star-schema model, DAX measures (rates, Cpk/Ppk, Pareto, SPC), validated against SQL and Python; interactive Overview, Pareto and SPC pages.
Notes: Cleaning decisions: 38 duplicates removed; 90 missing and 14 impossible diameters kept as rows but excluded from diameter statistics; two timestamp formats parsed. Control limits from the January baseline, which itself was not in control.